## Slide 1: SDN – Software Defined Networking

## Slide 2: Learning objectives
Understand the difference between traditional networking and SDN
Learn SDN architecture and key components
Explore SDN controllers and protocols
Simulating/experimenting with SDN
Discuss challenges and future directions

## Slide 3: Why SDN ?
Traditional networks are hardware-centric and vendor-specific
Complex to configure and scale
Slow to respond to changes or failures
SDN enables programmability, automation, and centralized control

## Slide 4: Traditional vs. SDN Networking
Traditional:
  distributed control plane, manual configuration
  static, complex architecture
  Inconsistent policies
  inability to scale
  vendor dependence
SDN:
  centralized control plane, software-defined policies
  decouples control plane and data plane
  adaptability and maintainability
  automation
  on-demand scaling

## Slide 5: Typical network architecture (traditional and SDN)

## Slide 6: Traditional networking

## Slide 7: Software Defined Networking

## Slide 8: SDN Core Principles
Separation of control and data plane
Programmable network behavior
Centralized network intelligence
Open interfaces (APIs) for automation
SDN makes networks “software-controllable” like cloud systems

## Slide 9: SDN Architecture Overview
Infrastructure Layer – switches, routers
Control Layer – SDN controller, network OS
Application Layer – apps using network APIs

## Slide 10: SDN architecture

## Slide 11: SDN Infrastructure Layer
Physical or virtual switches
OpenFlow-capable devices
Forwarding devices execute controller instructions

## Slide 12: SDN Control Layer
Centralized SDN Controller
Maintains global network view
Computes paths and distributes flow rules
Examples: ONOS, OpenDaylight, Ryu, Floodlight

## Slide 13: SDN Controller functions

## Slide 14: SDN Application Layer
Network applications use northbound APIs
Examples:
  Traffic engineering
  Security automation
  QoS and monitoring
  apps can dynamically react to network state

## Slide 15: SDN APIs
Southbound APIs: OpenFlow, NETCONF/YANG, P4Runtime
Northbound APIs: REST, intent-based interfaces, higher-level orchestration
Southbound APIs control switches; northbound API enable apps to control network

## Slide 16: OpenFlow Basics
Core protocol for SDN
Flow tables in switches
Controller instructs switches on packet forwarding
Match-action rules: match packet → apply action

## Slide 17: OpenFlow

## Slide 18: OpenFlow switch

## Slide 19: OpenFlow – FlowTable structure
Each packet entering the switch passes through one or more flow tables
Each packet is matched to a flowtable entry and sent to an egress port or to another flow table

## Slide 20: OpenFlow – Ingress processing of a packet

## Slide 21: OpenFlow – Egress processing of a packet

## Slide 22: Programmable Data Plane
P4 language for custom packet processing
Programmable switch pipelines
Use cases: load balancing, custom packet headers, telemetry

## Slide 23: SDN Virtualization
Overlay networks: VXLAN, GRE, Geneve
NFV vs SDN – complementary concepts
Virtual switches: Open vSwitch, VPP

## Slide 24: SDN Controllers
Centralized intelligence for network automation
Features: topology discovery, flow rule distribution, traffic engineering
Popular controllers: OpenDaylight, ONOS, Ryu, Floodlight

## Slide 25: SDN Use Cases: Data Centers
Multi-tenant networks with isolation
Automated provisioning and scaling
East-west traffic optimization

## Slide 26: SDN Use Cases: Service Providers
5G network slicing
WAN SDN for traffic optimization
Carrier-grade traffic engineering

## Slide 27: SDN Use Cases: Enterprise & Campus
Centralized policy and network segmentation
Dynamic QoS for applications
Identity-based access control and security automation

## Slide 28: SDN Tools & Emulation
Mininet – virtual networks for labs
GNS3 / EVE-NG – industry-grade emulation
P4 Development Tools – BMv2 switch, Tofino, P4Runtime

## Slide 29: SDN Challenges
Controller scalability and consistency
Reliability and single point of failure
Security: controller attacks, API misuse
Standardization issues: multiple southbound protocols